## Slide 1
IMR Salinity Sample Tracker
A new digital labeling workflow for salinity sample collection, measurement, and upload to PhysChem
Institute of Marine Research · 2025

## Slide 2
The Old Way
❌ Paper logbooks — easy to lose, hard to read
❌ Manual lookup in spreadsheets to match samples with CTD data
❌ Transcription errors when entering values into PhysChem
❌ No clear link between the physical bottle and the database entry
❌ Time-consuming — one person re-entering data from logbooks in the lab

## Slide 3
New Workflow — 3 Steps
🚢
On the Ship
Upload BTL file (or manual entry) → System registers sample → Print QR label → Stick label on bottle
→
🔬
In the Lab
Scan QR code on label → Measurement page opens instantly → Enter PSAL_LAB value → Click Upload
→
✅
In PhysChem
Value uploaded automatically → Correct mission, cast & bottle → matched by time, position & depth → View confirmation link

## Slide 4
The Label
IMR Salinity Sample
G.O. Sars
2025-06-12 14:32 UTC
69.2341°N
18.4521°E
Depth: 250.0 m
Bottle: 12
Cruise: 2025707
a3f9c12e
QR
a3f9c12e
50 × 30 mm Phomemo M110 printer
✔ Vessel, time, position, depth — printed clearly
✔ Bottle & depth in bold — easy to read on deck
✔ QR code → opens lab measurement page directly
✔ 8-character ID — short, unique, scannable

## Slide 5
In the Lab — Measurement Page
1. Scan QR code → measurement page opens (browser, phone, tablet, scanner)
2. Page shows: sample metadata | CTD sensor PSAL values from PhysChem
3. Enter PSAL_LAB value → Upload
4. System finds matching mission / operation / bottle automatically
5. Success page shows confirmation + link to PhysChem entry
Token: paste a 1-hour PhysChem token once per session — button stays disabled until token is active
Replicates: scan again → 'Add Additional Measurement' → new ordinal, original never overwritten

## Slide 6
Key Benefits
⚡ Fast
BTL file upload registers an entire CTD cast in seconds
🔗 Traceable
Every bottle linked by QR code from deck to PhysChem
🛡️ Safe
No overwrites — replicates get new ordinals automatically
📊 Complete
CSV export with all measurements, ordinals & PhysChem IDs
🌐 Accessible
Works on any browser — phone, tablet, PC
🔍 Auditable
All samples visible at /samples with status tracking

## Slide 7
Getting Started
Browser → http://nautilus.imr.no:8000 (IMR network only)
On the ship:
• Home page → drag & drop BTL file → select bottles → register → print labels
• Stick label on dry bottle before leaving the CTD deck
In the lab:
• Get a PhysChem token from https://physchem-token-test.hi.no
• Scan QR → enter value → upload
Questions / issues: sebastian.menze@imr.no